## Slide 1
micro:bit CreateAI: Explore AI Through Movement
Sarah Rankin
Centre of Excellence – Digital Innovation Lead
EECD

## Slide 3
What is CreateAI?
micro:bit Powered
Classify and collect accelerometer data
Web-based
Nothing to download to add to micro:bit
Connects to MakeCode
Once the AI model is trained, import into MakeCode
for use in machine learning projects

## Slide 4
What is Machine Learning?
AI Technology
Machine learning lets computers learn from data and make decisions.
Real-World Uses
Powers smart fitness trackers and photo tagging systems.
Educational Value
Works with small data sets, making it ideal for classroom use.

## Slide 5
What You Need
Hardware
micro:bit V2
USB cable
Batteries and battery pack
Strap or holder for attachment (optional)
Computer
Desktop, laptop or Chromebook
Chrome or Edge browser
Not Supported
iPads or tablets
micro:bit classroom
micro:bit V1 for running models

## Slide 6
Connecting Your micro:bit
Connect micro:bit to laptop
Use Bluetooth, USB cable and battery pack
Follow On-Screen Instructions
CreateAI guides you through setup
Test Connection
Once connected, you're ready to record movement data.

## Slide 7
Recording Data Samples
Hold or Attach micro:bit
Secure to wrist, ankle, or hold in hand.
Name Your Actions
Choose movements like clapping, waving, or jumping.
Record Samples
Collect at least 3 samples per action.
Check Data Quality
Remove outliers and record more if needed.

## Slide 8
Training and Testing Your Model
Train Model
Press "Train model" when you have enough data.
Test Recognition
Try each action to see if the model recognizes it.
Adjust Settings
Change recognition threshold if needed.
Improve Model
Add more samples or actions to enhance accuracy.

## Slide 9
Coding with Your Model
Edit in MakeCode
Use ML blocks that represent your trained actions. Add your own code to create interactive projects.
ML Block Types
Use "on ML start," "on ML stop," "is ML detected," and "certainty %" blocks to build your program.
Download and Run
Transfer your model and code to the micro:bit V2. Use it anywhere, away from your computer.