## Slide 1
Welcome
to
Roofing Sandwiches:
A Tasty Exploration

## Slide 2
What is Commercial Roofing?
What are potentials careers in Commercial Roofing?

## Slide 3
Commercial Roofing is…
Commercial roofing/roofers install, repair or replace flat roofs as well as sloped roofs They use a variety of materials such as corrugated metal, wood, membranes, insulation and shingles They must consider many factors such as regional weather, weight expectancy, flat versus sloped roof and available roofing materials to use, as well as their sequence.

## Slide 4: Careers in Commercial Roofing
Roofer
Observer
Estimator
Consultant
Superintendent

## Slide 5: Meet Edgar!
NBRCA Roofing
Training Instructor

## Slide 6: Life at the NBRCA Roofing Training Centre
NBJobs.ca Careers - Roofers

## Slide 7: Roofing Materials and Layers
Roof Deck
Vapour Retarder
Deck Cover
Cover Board
Flashing
Membrane
Insulation

## Slide 8: Roof Deck
A roof deck is installed as part of the building structure to keep the building together and support the roof system and the outside elements (rain, snow, ice, vegetated roof (plants), etc.) and are typically either wood, steel or concrete. When a roofer gets to the job site, a roof deck should already be in place. This is where a roofer's job begins.

## Slide 9: Deck Cover
The deck cover is the first step in building a roof. Typically used over a steel deck and only as required on wood or concrete decks if they are uneven. This is used to prepare the rest of the roof installation so it is solid and flat (gypsum board and plywood are common elements)

## Slide 10: Vapour Retarder
The vapour retarder (barrier), which slows the movement of interior air/water (vapour) into the roof system and the exterior air/water (vapour) from the roof system into the building.

## Slide 11: Insulation
Insulation insulates the roof of the building. It comes in various shapes, sizes and material types with various R- Values. It prevents loss of heat from the building and keeps the occupants of the building comfortable.

## Slide 12: Cover Board
Coverboards are used to separate the insulation from the membrane. This is to allow movement from the two types of roof components caused by changes in temperature. The coverboard saves the membrane from potential ripping.

## Slide 13: Flashing
Flashing is a thin sheet of material used to cover any remaining gaps or openings left around seams and edges. This will prevent water from entering where it's not supposed to go.

## Slide 14: Membrane
A membrane is the waterproofing layer, keeping rain, snow, ice, wind, etc. outside.
Two common types are modified bitumen and single-ply (EPDM, PVC, TPO).

## Slide 15: Exploration of Materials
What from your kit materials best represents each layer?

## Slide 16: Exploration of Materials
Roof Deck
Vapour Retarder
Deck Cover
Cover Board
Flashing
Membrane
Insulation

## Slide 17: ROOFING 101

## Slide 18: Roofing Building Challenge
Used with permission from RCABC
Each sandwich MUST:
Include all 7 layers of a flat roof
Sandwich built in the correct order
At least one seam in top membrane
Demonstrate clean roofing skills (no glue leaking, flat roof, no holes in edge flashing)
Time to BUILD!!

## Slide 19: Roofing Building Challenge
Used with permission from RCABC
Insulation (foam sheets) - 1 or 2 sheets
Cover Board (cardboard paper)
Membrane (shelf liner) with a seam
Flashing (tinfoil)
Vapour Retarder (wax paper)
Roof Deck (BBQ tray)
Deck Cover (meranti plywood)
Peel and stick to
Strips to close gaps and lap over sides
Tack or glue to
Tack or glue to
Tack or glue to
Place inside of

## Slide 20
PAIR & SHARE
1 CHALLENGE
Share one thing that you/your team had to overcome.
1 VICTORY
Share one thing that you/your team did well!